## Slide 1: Market Primer | DDG-51 construction dollars flow through prime yards, Navy-procured GFE primes, and yard-side suppliers
DDG-51 supplier TAM / Market primer
Preliminary
Read: DDG-51 construction is layered: Navy funding, two prime yards, Navy-procured GFE, and the yard-side supplier layer sized in this deck.
U.S. NAVY SCN
Line Item 2122
new-construction funding
GD Bath Iron Works
prime-yard node
HII Ingalls
prime-yard node and distributed-network context
IN-SCOPE SUPPLIER LANE
yard-side supplier work sized by the deck
non-GFE new-construction supplier TAM
Excluded lanes are context, not the sized supplier TAM
GFE
Navy-procured combat-system primes
WEAPONS
WPN and OPN missile and ordnance flows
SUSTAINMENT
depot, repair, modernization
FFATA
evidence source, not definition
Legend: blue lane = sized non-GFE supplier work; gray tags = exclusions or evidence lenses; dashed lines = context/evidence only.
Market layer: the prime yards are pass-through and self-perform nodes, not target suppliers.
Evidence layer: FFATA-visible subawards help classify work, but do not set the denominator.
Sources: (1) U.S. Navy FY2027 SCN Justification Book, LI 2122; (2) FAR Part 45 and FAR 52.245-1, Government Property; (3) FAR 52.204-10

## Slide 2: Executive Summary | DDG-51 supplier TAM averages ~$573M per year, with ~$327M per year in broad component SAM
DDG-51 supplier TAM / Answer
Preliminary
Answer convention: headline values are average annual FY22-27; cumulative values are secondary context, not a run-rate.
SUPPLIER TAM
~$573M per year
($3.44B FY22-27)
BROAD SAM
~$327M per year
($1.96B FY22-27)
BC STREAM
~$365M per year
~$2.19B cumulative
AP AND LLTM
~$208M per year
~$1.25B cumulative
BROAD SAM SHARE
57.1% of TAM
scenario, not SOM
PER HULL
~$265M
13 in-window hulls
Answer: supplier TAM is ~$573M per year after non-GFE and MYP-corrected scope gates.
Serviceable menu: broad component SAM is the largest scenario at ~$327M per year.
Discipline: SAM is not SOM and the scenarios are never summed.
Nominal $M per year; average annual FY22-27 unless noted. FY22-27 cumulative values shown in parentheses. Excludes SOM and capture.
Sources: (1) U.S. Navy FY2022-FY2027 SCN Justification Books, LI 2122; (2) DoW DDG-51 contract announcements, July 2022 to May 2026; (3) SAM.gov Subaward Reporting Public API

## Slide 3: Scope | The analysis sizes non-GFE new-construction supplier work, not total DDG spend
DDG-51 supplier TAM / Scope
Preliminary
IN SCOPE sized in TAM and SAM | OUT OF SCOPE not in TAM
DDG-51 Flight IIA and Flight III new construction | DDG-1000 Zumwalt (out of class, closed)
SCN Line Item 2122 appropriation | WPN and OPN weapons procurement
Basic Construction supplier work | Aegis, SPY-6, Mk 41 VLS, Mk 45, LM2500, SEWIP, CIWS, and other GFE-heavy prime flows
AP and LLTM supplier-addressable material | Sustainment, depot, ship repair, design-only, and MIB
Work performed away from BIW, Ingalls, GFE prime sites, and Navy-directed flows | Contaminants such as the IVECO Mk 110 gun and Thales ESSM artifacts
Boundary cue: total DDG spend, then non-GFE new-construction base, then supplier-addressable TAM, then the SAM work-type menu.
Sources: (1) CRS RL32109, Navy DDG-51 and DDG-1000 Destroyer Programs; (2) U.S. Navy FY2027 SCN Justification Book, LI 2122; (3) FAR 52.204-10 and FAR Part 45

## Slide 4: Cost Funnel | Basic Construction is the supplier-addressable base after excluding GFE-heavy cost categories
DDG-51 supplier TAM / Cost funnel
Preliminary
FY24 DDG-51 cost categories, both ships
Chart: 
| Basic Construction (60.5%) | Electronics and Ordnance GFE (32.9%) | Other smaller categories (6.6%)
FY24 cost category value | 3322 | 1807 | 363
TOTAL SHIP ESTIMATE
~$5,492M
Basic Construction is ~$3,322M, or 60.5% of total.
Denominator decision
1. TOTAL SHIP COST
Too broad for supplier TAM
2. BASIC CONSTRUCTION
Supplier-addressable starting base
3. NEXT CORRECTION
Apply the MYP-corrected supplier coefficient
Sources: (1) U.S. Navy FY2027 SCN Justification Book, LI 2122, Exhibit P-5c; (2) Congressional Research Service, Navy DDG-51 and DDG-1000 Destroyer Programs, RL32109; (3) FAR Part 45 and FAR 52.245-1

## Slide 5: MYP Redaction | Restoring the redacted multiyear masters corrects the outside-yards artifact to ~33%
DDG-51 supplier TAM / Denominator correction
Preliminary
MYP-corrected place-of-performance distribution
Chart: 
| Corrected POP distribution
BIW site | 0.29
Ingalls site | 0.336
Other-US supplier | 0.315
Foreign | 0.013
Unparsed | 0.045
Outside-yards share after restoring redacted MYP masters
Chart: 
| MYP-corrected | Disclosed-only artifact, do not headline
Outside-yards share | 0.328 | 0.87
RECONSTRUCTED FY23-27 MYP MASTERS
~$14.58B
BIW plus Ingalls masters folded back
GATED POP CORPUS INCL. MASTERS
~$21.71B
distribution base for correction
What changed
The FY23-27 BIW and Ingalls multiyear masters disclose work locations but redact dollar values.
Those masters are large and yard-heavy, so omitting their dollars over-weights disclosed GFE actions.
The model restores ~$14.58B of master value before applying the Basic Construction supplier coefficient.
Use the corrected ~33% outside-yards view going forward, not the disclosed-only artifact.
Sources: (1) DoD daily contract announcements, war.gov articles 3479250 (Aug. 1, 2023) and 3491276 (Aug. 11, 2023); (2) 41 U.S. Code 2101 et seq. and FAR 2.101 and FAR 3.104; (3) U.S. Naval Institute News reporting on the FY23-27 DDG-51 multiyear award

## Slide 6: TAM Methodology | TAM combines Basic Construction supplier work with AP and LLTM supplier material
DDG-51 supplier TAM / Method
Preliminary
Method: supplier TAM is the sum of two separately gated supplier streams.
BASIC CONSTRUCTION STREAM
BC base: ~$17.47B cumulative
Times 12.5% MYP-corrected supplier coefficient
Equals ~$365M per year (~$2.19B cumulative)
PLUS
AP AND LLTM STREAM
CY AP after 80.0% ship-construction share: ~$1.47B
Times 85.0% AP supplier coefficient
Equals ~$208M per year (~$1.25B cumulative)
PORTFOLIO SUPPLIER TAM
~$573M per year
(~$3.44B FY22-27 cumulative)
Guardrail: the BC coefficient is 12.5% on the MYP-corrected non-GFE corpus. It is not the ~32.8% outside-yards POP share, nor the disclosed-only ~87% artifact.
Nominal $M per year; average annual FY22-27 unless noted. FY22-27 cumulative values shown in parentheses. Excludes SOM and capture.
Sources: (1) U.S. Navy FY2022-FY2027 SCN Justification Books, LI 2122; (2) DoD DDG-51 daily contract announcements, July 2022 to May 2026; (3) SAM.gov Acquisition Subaward Reporting Public API

## Slide 7: Annual TAM Build | The corrected model yields ~$573M per year of supplier TAM
DDG-51 supplier TAM / TAM build
Preliminary
Average annual supplier TAM build, FY22-27
Chart: 
| BC construction base | Less prime, co-prime, GFE POP | BC-stream supplier TAM | Add AP and LLTM stream | Portfolio supplier TAM
_Base | 365.3 | 365.3
Increase | 207.8
Decrease | 2546.5
Total | 2911.8 | 365.3 | 573.1
Cumulative bridge | FY22-27
BC base | ~$17.47B
Removed | ~$15.28B
BC stream | ~$2.19B
AP and LLTM | ~$1.25B
Portfolio TAM | ~$3.44B
Nominal $M per year; average annual FY22-27 unless noted. FY22-27 cumulative values shown in parentheses. Excludes SOM and capture.
Sources: (1) U.S. Navy FY2022-FY2027 SCN Justification Books, LI 2122; (2) DoD DDG-51 daily contract announcements, July 2022 to May 2026; (3) SAM.gov Acquisition Subaward Reporting Public API

## Slide 8: TAM Timing | Annual supplier TAM is lumpy, with the FY26 spike driven by AP and LLTM
DDG-51 supplier TAM / Timing
Preliminary
Supplier TAM by fiscal year and stream
Chart: 
| FY22 | FY23 | FY24 | FY25 | FY26 | FY27
BC stream | 245.9 | 571.9 | 416.9 | 580.7 | 35.5 | 341.2
AP and LLTM stream | 0 | 0 | 0 | 56.6 | 1190 | 0
Average-annual convention
~$573M per year
FY26 is not the run-rate
~$1.23B, driven by AP and LLTM
Nominal $M per year; average annual FY22-27 unless noted. FY22-27 cumulative values shown in parentheses. Excludes SOM and capture.
Sources: (1) U.S. Navy FY2022-FY2027 SCN Justification Books, LI 2122; (2) DoD DDG-51 daily contract announcements, July 2022 to May 2026; (3) SAM.gov Acquisition Subaward Reporting Public API

## Slide 9: SAM Taxonomy | SAM is a work-type bucket menu, not a capture forecast
DDG-51 supplier TAM / SAM taxonomy
Preliminary
PORTFOLIO TAM
~$573M per year
(~$3.44B FY22 to FY27 cumulative)
STRUCTURAL FABRICATION
and pre-outfit
MACHINING
precision and mechanical
CASTINGS AND FORGINGS
metal components
PIPING, VALVES, AND PUMPS
HM&E path
ELECTRICAL AND POWER
standalone scenario
HVAC AND VENTILATION
HM&E path
COATINGS AND INSULATION
modular path
UNBUCKETED AND AMBIGUOUS
~$246M per year
42.9% of TAM
SAM: selects from named work-type buckets inside TAM. It does not apply win probability, and scenarios are not additive.
Bucket | Metal | HM&E | Elec | Modular | Broad
Structural | Yes | No | No | Yes | Yes
Machining | Yes | Yes | No | No | Yes
Castings | Yes | No | No | No | Yes
Piping | No | Yes | No | No | Yes
Electrical | No | No | Yes | No | Yes
HVAC | No | Yes | No | No | Yes
Coatings | No | No | No | Yes | Yes
Sources: (1) SAM.gov Acquisition Subaward Reporting Public API; (2) FAR 52.204-10; (3) U.S. Navy FY2022-FY2027 SCN Justification Books, LI 2122

## Slide 10: Work-Type Allocation | Residual ambiguity is the largest line, while electrical and structural are the largest named buckets
DDG-51 supplier TAM / Work-type allocation
Preliminary
Portfolio TAM allocation by work type, average annual FY22-27
Chart: 
| Unbucketed / ambiguous (42.9%) | Electrical and power (23.0%) | Structural fabrication and pre-outfit (17.7%) | Machining (11.4%) | Piping, valves, and pumps (2.3%) | HVAC and ventilation (1.7%) | Coatings and insulation (0.5%) | Castings and forgings (0.5%)
Average annual TAM | 245.8 | 131.8 | 101.4 | 65.6 | 13 | 9.9 | 2.8 | 2.7
RESIDUAL IS EVIDENCE AMBIGUITY
The seven named buckets sum to broad component SAM; the gray residual remains in TAM but outside broad SAM.
Nominal $M per year; average annual FY22-27 unless noted. FY22-27 cumulative values shown in parentheses. Excludes SOM and capture.
Sources: (1) SAM.gov Acquisition Subaward Reporting Public API; (2) FAR 52.204-10; (3) U.S. Navy FY2022-FY2027 SCN Justification Books, LI 2122

## Slide 11: SAM Scenarios | Broad component manufacturing represents ~$327M per year of serviceable market
DDG-51 supplier TAM / SAM scenarios
Preliminary
SAM scenarios, average annual FY22-27
Chart: 
| Broad component manufacturing (57.1%) | Metal components (29.6%) | Electrical and power (23.0%) | Modular assemblies (18.2%) | HM&E components (15.4%)
Average annual SAM | 327.3 | 169.7 | 131.8 | 104.3 | 88.5
Bucket | Metal | HM&E | Elec | Modular | Broad
Structural | Yes | No | No | Yes | Yes
Machining | Yes | Yes | No | No | Yes
Castings | Yes | No | No | No | Yes
Piping | No | Yes | No | No | Yes
Electrical | No | No | Yes | No | Yes
HVAC | No | Yes | No | No | Yes
Coatings | No | No | No | Yes | Yes
Nominal $M per year; average annual FY22-27 unless noted. FY22-27 cumulative values shown in parentheses. Excludes SOM and capture.
Sources: (1) SAM.gov Acquisition Subaward Reporting Public API; (2) FAR 52.204-10; (3) U.S. Navy FY2022-FY2027 SCN Justification Books, LI 2122

## Slide 12: Supplier Landscape | Visible supplier flow is concentrated among specialized defense manufacturers
DDG-51 supplier TAM / Supplier landscape
Preliminary
Top visible first-tier suppliers by lifetime flow, $M
Chart: 
| Leonardo SpA | Arctic Slope Regional Corp | Major Tool and Machine | General Dynamics Corp | General Electric Co | Rolls-Royce Holdings plc | Northrop Grumman Corp | Johnson Controls Navy Systems | Advanced Sciences and Technologies | CAES Systems LLC
Lifetime visible flow | 1810.3 | 987.4 | 816.1 | 372 | 335.6 | 257.2 | 249.3 | 178.2 | 174 | 169.2
Example | Role | Caveat
Leonardo via DRS | Electrical and VLS | Foreign parent, U.S. work sites
Arctic Slope | Engineering services | Not a pure component manufacturer
Major Tool | Machining | Clean physical-components proof point
General Dynamics | Prime-affiliated | Do not read as third-party wedge
GE and Rolls-Royce | Propulsion | Visible flow can understate vertical integration
Lifetime visible first-tier subaward flow per parent vendor; a floor, not the full supplier base. Names only, no logos.
Sources: (1) SAM.gov Acquisition Subaward Reporting Public API; (2) SAM.gov Entity Management API; (3) FAR 52.204-10

## Slide 13: FFATA Visibility Gap | FFATA is evidence, not the market-size denominator
DDG-51 supplier TAM / Visibility gap
Preliminary
Cumulative FFATA-visible flow vs estimated yard-side outsourcing, $M
Chart: 
| FFATA-visible yard-side flow (~$2.73B) | Estimated outsourcing, low (~$11.31B) | Estimated outsourcing, midpoint (~$13.57B) | Estimated outsourcing, high (~$16.16B)
Cumulative FY2016-FY2027 | 2728.6 | 11311.4 | 13573.7 | 16159.2
What public FFATA misses
DIRECT MATERIAL
Booked as direct cost, not a subcontract
LOWER TIERS
A sub's sub is outside FFATA visibility
STANDING AGREEMENTS
Long-term supplier deals may not sit under a prime PIID
THRESHOLD AND LAG
Sub-$30,000 actions plus 12-30 month reporting lag
REPORTING GAP
BIW under-reporting is acute but not the whole gap
Visible flow is ~20.1%
of the midpoint estimate on a cumulative basis
FFATA provides public evidence of the supplier base; it does not capture the full true flow. Values are cumulative FY2016-FY2027.
Sources: (1) SAM.gov Acquisition Subaward Reporting Public API; (2) HII and General Dynamics Form 10-K filings; (3) U.S. BLS OEWS, NAICS 336611

## Slide 14: Market Direction | Distributed shipbuilding points toward more external production capacity
DDG-51 supplier TAM / Market direction
Preliminary
Distributed-shipbuilding signals, FY2024 Q3 to FY2026 Q1
Period | Source | Signal | Implication
FY24 Q3 | HII | Outsourcing over 1 million hours in 2024; planned increase of more than 30% in 2025 | Outsourcing is now a named lever
FY25 Q4 | HII | Outsourcing doubled year over year in 2025; +30% planned in 2026; over 23 vendors established | Supplier network is scaling
FY26 Q1 | HII | On track to grow outsourcing hours ~30%; first 2 of 32 units in yard from partners on DDG 137 | Distributed work reaching the DDG line
FY25 Q4 | General Dynamics | Supply chain remains the gating item (Electric Boat context); no comparable DDG outsourcing-hours target | Constraint is broad, not a DDG plan
FY25-FY26 | Navy and GAO | Shipbuilders already outsource to overcome constrained physical space; distributed production policy | Directional tailwind
Direction: external production capacity is expanding, especially at HII Ingalls.
Asymmetry: HII has the clearest public commitment; GD signals supplier constraints, submarine-centric.
Scope: directional only — it does not change the FY22-27 TAM math without a refreshed model.
Sources: (1) HII quarterly earnings materials, FY2024 Q3-FY2026 Q1; (2) General Dynamics earnings materials, FY2025 Q4-FY2026 Q1; (3) GAO-25-106286

## Slide 15: Implications | Prioritization depends on product scope, qualification burden, and confidence in bucket visibility
DDG-51 supplier TAM / Implications
Preliminary
Scenario prioritization scorecard, average annual FY22-27
Scenario | Avg annual | Cumulative | TAM share | Confidence | Priority read
Broad component manufacturing | ~$327M per year | ~$1.96B | 57.1% | Medium | Envelope, not a single wedge
Metal components | ~$170M per year | ~$1.02B | 29.6% | Medium-high | Largest targeted scenario; high if fabrication or machining scope fits
Electrical and power | ~$132M per year | ~$791M | 23.0% | Medium | Largest single named bucket; high but qualification-heavy
Modular assemblies | ~$104M per year | ~$626M | 18.2% | Medium | Strategic distributed-capacity lane; smaller in the current model
HM&E components | ~$89M per year | ~$531M | 15.4% | Medium-low | Selective, product-by-product; evidence-dependent
Where-to-play screen, not SOM. Prioritization depends on product scope, qualification burden, and confidence in bucket visibility.
Nominal $M per year; average annual FY22-27 unless noted. FY22-27 cumulative values shown in parentheses. Excludes SOM and capture.
Sources: (1) SAM.gov Acquisition Subaward Reporting Public API; (2) U.S. Navy FY2022-FY2027 SCN Justification Books, LI 2122; (3) GAO-25-106286

## Slide 16: Definitions and Scope | Total ship cost, SCN, Basic Construction, FFATA-visible flow, and supplier-addressable TAM each do a different job
DDG-51 supplier TAM / Definitions and scope
Preliminary
Denominator and scope ledger, DDG-51 supplier TAM
Denominator | Definition | Included examples | Excluded examples | Where used
Total ship cost | P-5c Total Ship Estimate by procurement year | Basic Construction, Electronics, Ordnance, Plans, HM&E, Other | WPN and OPN weapons, depot sustainment | Cost funnel context only
SCN LI 2122 | DDG-51 Class Destroyer line item in the Navy SCN budget books | DDG-51 Flight IIA and Flight III new construction | DDG-1000 Zumwalt (LI 2119), cruiser modernization, depot repair | Scope gate and schedule
Basic Construction base | Prime construction layer flowing through BIW and Ingalls prime contracts | Yard work and yard-side supplier work | Navy-procured Aegis, SPY-6, Mk 41, Mk 45, LM2500, SEWIP | BC stream TAM
AP and LLTM base | Current-year advance procurement and long-lead material that is supplier-addressable | Ship-construction EOQ and long-lead material after the non-GFE filter | AWS EOQ, Other GFE, VLS and weapons AP | AP and LLTM stream TAM
FFATA-visible flow | First-tier subawards reported to FSRS and surfaced through SAM.gov | Reportable first-tier subcontracts above the threshold | Direct material, lower-tier subs, standing agreements, sub-threshold tail | Evidence and bucket rules
Supplier-addressable TAM | BC base times the BC supplier coefficient, plus AP and LLTM base times the AP coefficient | Non-GFE new-construction supplier work away from the prime yards | GFE, WPN and OPN weapons, sustainment, design-only, SOM and capture | Headline market size
SAM scenarios | Selected work-type bucket menus within TAM | Broad, metal, electrical, modular, HM&E | Unbucketed residual unless later classified, capture probability | Where-to-play menu
TAM window: FY2022 to FY2027; the wiki framing window is FY2018 to FY2027.
In scope: DDG-51 new-construction PIID set, two prime yards plus major GFE primes.
Excluded: Zumwalt, depot sustainment, WPN and OPN weapons, GFE combat-system content, and contaminants.
Boundary cue: the deck sizes non-GFE new-construction supplier work within Basic Construction and AP and LLTM. SAM is a strict subset of TAM, never SOM.
Sources: (1) U.S. Navy FY2027 SCN Justification Book, LI 2122, Exhibit P-5c; (2) FAR 52.204-10 and 48 C.F.R. Part 45; (3) CRS, Navy DDG-51 and DDG-1000 Destroyer Programs, RL32109

## Slide 17: TAM Calculation | The annual headline is the FY22-27 cumulative two-stream model divided by six
DDG-51 supplier TAM / TAM calculation
Preliminary
Average annual: FY22-27 cumulative divided by six; not a steady run-rate. The per-FY TAM profile is lumpy, with a FY26 AP spike.
Step | FY22-27 cumulative $M | Avg $M per year | Coefficient | Model source or note
Basic Construction base | 17,471.0 | 2,911.8 | n.a. | P-5c BC base, LI 2122
BC supplier coefficient (MYP-corrected) | n.a. | n.a. | 12.5% | Other-US and foreign POP
BC-stream supplier TAM | 2,192.0 | 365.3 | applied | Base times coefficient
CY AP in-window (FY25 to FY27) | 1,833.2 | 305.5 | n.a. | FY22-24 sit in Prior Years
Ship-construction share of CY AP | 1,466.6 | 244.4 | 80.0% | Non-GFE share
Non-GFE AP base | 1,466.6 | 244.4 | n.a. | AP base after the share
AP and LLTM supplier coefficient | n.a. | n.a. | 85.0% | Inputs assumption knob
AP and LLTM stream TAM | 1,246.6 | 207.8 | applied | Second stream
Portfolio supplier TAM | 3,438.6 | 573.1 | n.a. | Headline TAM
Average annual convention | 3,438.6 | 573.1 | divide by 6 | Not a steady run-rate
CUMULATIVE BRIDGE, $M
BC-stream supplier TAM: ~2,192.0
AP and LLTM stream TAM: ~1,246.6
Portfolio supplier TAM: ~3,438.6
Divide by 6: ~573.1 per year
13 in-window hulls (award FY22-27). Supplier TAM per hull ~$265M; BC TAM per hull ~$169M. BC base ~$17.47B less POP removal leaves the ~$2.19B BC stream.
Nominal $M per year; average annual FY22-27 unless noted. FY22-27 cumulative values shown in parentheses. Excludes SOM and capture.
Sources: (1) U.S. Navy FY2022-FY2027 SCN Justification Books, LI 2122, Exhibit P-5c; (2) U.S. Navy FY2027 SCN Justification Book, LI 2122, Exhibit P-40; (3) DoW DDG-51 contract announcements, July 2022 to May 2026

## Slide 18: MYP Correction | Folding the redacted $14.58B masters back into the corpus corrects outside-yards POP to about one third
DDG-51 supplier TAM / MYP correction
Preliminary
MYP master reconstruction and outside-yards POP correction
Item | Approx. $M | Reconstructed POP | Model use | Guardrail
BIW FY23-27 MYP master | 6,400 | Bath 86%, supplier 14% | PIID N00024-23-C-2305 | Redacted dollar value
Ingalls FY23-27 MYP master | 8,180 | Pascagoula 88%, supplier 12% | PIID N00024-23-C-2307 | Redacted dollar value
Combined reconstructed masters | 14,580 | Yard-heavy | 67.2% of gated corpus | Too large to ignore
Disclosed announcement corpus | 7,132 | 152 gated actions | Disclosed-only base | Over-weights GFE
Gated corpus incl. masters | 21,712 | All gated | Denominator for correction | Use for the corrected view
Corrected outside-yards POP | n.a. | 32.8% | Other-US and foreign | Defensible reading
Disclosed-only artifact | n.a. | 73.6% | Guardrail only | Do not headline
TAM sensitivity | 1,310 | Uplift | ~$3.44B corrected vs ~$2.13B disclosed-only | Method swing
Outside-yards POP share
Disclosed-only artifact
73.6%
MYP-corrected
32.8%
Read: the corrected view is about one third of the gated corpus, corrected to from the artifact.
Guardrail: do not headline the disclosed artifact; the ~32.8% outside-yards POP is not the 12.5% BC supplier coefficient.
Sources: (1) DoW DDG-51 contract announcements, Aug. 1 and Aug. 11, 2023; (2) 41 U.S. Code 2101 et seq. and FAR 2.101 and 3.104; (3) USNI News, Navy reporting on the FY23-27 DDG-51 multiyear master awards, 2023

## Slide 19: AP and LLTM Sensitivity | The AP and LLTM stream is assumption-driven and contributes about 36% of portfolio TAM
DDG-51 supplier TAM / AP and LLTM sensitivity
Preliminary
Step | Cum $M | Avg $M per year | Share or coeff. | Treatment note
CY Advance Procurement, in-window | 1,833.2 | 305.5 | n.a. | FY25-27 CY AP base
x ship-construction share | 1,466.6 | 244.4 | 80.0% | Strips AWS EOQ and other GFE
x AP and LLTM supplier coefficient | 1,246.6 | 207.8 | 85.0% | Inputs assumption (no AP POP corpus)
AP and LLTM stream TAM | 1,246.6 | 207.8 | 36.3% | Share of ~$3.44B portfolio TAM
Include: Ship Construction EOQ and supplier-addressable long-lead material.
Exclude: Aegis Weapon System EOQ, Other GFE, VLS, weapons and ordnance AP, WPN and OPN flows.
Already in BC: Power Conversion Modules moved into Basic Construction in FY23; do not re-add.
AP and LLTM cumulative TAM sensitivity, $M
Share | AP coeff 75% | AP coeff 85% | AP coeff 95%
70% | 962 | 1,091 | 1,219
80% | 1,100 | 1,247 | 1,393
90% | 1,237 | 1,403 | 1,568
Nominal $M per year; average annual FY22-27 unless noted. FY22-27 cumulative values shown in parentheses. Excludes SOM and capture.
Sources: (1) U.S. Navy FY2022-FY2027 SCN Justification Books, Line Item 2122; (2) CRS, Navy DDG-51 and DDG-1000 Destroyer Programs, RL32109; (3) DoD daily contract announcement, DDG 51 FY23-27 multiyear award, Aug. 1, 2023

## Slide 20: FFATA Limitations | Visible first-tier subawards are a floor and evidence base, not the market denominator
DDG-51 supplier TAM / FFATA limitations
Preliminary
Public-data element | What it captures | What it misses | Implication for deck use
FFATA first-tier subawards | Direct prime-to-sub subcontracts above the $30,000 threshold | Lower-tier suppliers and sub-threshold actions | Visible floor and evidence base
SAM.gov published and deleted records | FSRS records surfaced through the SAM.gov API (no per-PIID cap) | Reporting lag of 12 to 30 months and late corrections | Longitudinal evidence with a timing caveat
Yard-prime PIID filings | Yard-side filings by BIW and Ingalls | Direct material booked as direct cost and standing agreements | Supports the supplier landscape, not the denominator
Vendor and description fields | Visible supplier names and award descriptions | Incomplete NAICS and UEI resolution | Bucket evidence for SAM classification
SAM.gov Entity Management enrichment | Entity attributes, country, and validation support | Corporate-primary NAICS, not action-level work type | Useful for cleaning and enrichment
USAspending cross-validation | A cross-check against the federal spending view | Truncation at about 2,500 records per PIID and timing differences | Triangulation only; SAM.gov is canonical
Cumulative yard-side view | Value
FFATA visible | ~$2.73B
Estimated low | ~$11.31B
Estimated midpoint | ~$13.57B
Estimated high | ~$16.16B
Visible share at midpoint | 20.1%
What FFATA misses: direct material booked as direct cost (~$400 to 700M per year), lower-tier subcontracts, BIW under-reporting, long-term supplier agreements, sub-$30,000 tail, and 12 to 30 month reporting lag.
Sources: (1) FAR 52.204-10; (2) SAM.gov Acquisition Subaward Reporting Public API; (3) GAO-25-106286

## Slide 21: Bucket Rules and Supplier Evidence | Description-led classification maps subawards into seven target work types, with an explicit residual
DDG-51 supplier TAM / Bucket rules
Preliminary
Bucket definitions, scale, and supplier evidence
Bucket | Inclusion rule | Avg annual | FY22-27 cum. | Supplier evidence | Scenarios
Structural fab and pre-outfit | Hull sections, fabricated structural metal, deckhouse, pre-outfit modules | ~$101M | ~$608M | Major Tool and Machine; Superior Electromechanical; Leonardo via DRS | metal, modular, broad
Machining | Machine shops, precision machining, mechanical power transmission | ~$66M | ~$394M | Major Tool and Machine; Rolls-Royce; Timken Gears and Services | metal, HM&E, broad
Castings and forgings | Iron and steel forging, steel foundries, cast components | ~$3M | ~$16M | Ellwood Group | metal, broad
Piping, valves, and pumps | Industrial valves, pumps, manifolds, pipe and fittings, hydraulics | ~$13M | ~$78M | Curtiss-Wright; CIRCOR; Leslie Controls (vendor overrides) | HM&E, broad
Electrical and power | Switchgear, switchboards, cable, generators, motors, power distribution | ~$132M | ~$791M | Leonardo via DRS; General Electric; DRS Naval | electrical, broad
HVAC and ventilation | Air-conditioning, chilled water, warm-air heating, shipboard ventilation | ~$10M | ~$59M | Johnson Controls Navy Systems | HM&E, broad
Coatings and insulation | Coatings, paint, deck covering, insulation, rubber and synthetic | ~$3M | ~$17M | M.S.M. Industries; Espey Mfg. and Electronics | modular, broad
Unbucketed / ambiguous residual | Insufficient description, ambiguous scope, or evidence too thin to classify; do not force-classify | ~$246M | ~$1.47B | Held explicit; not assigned to a named bucket | excluded from broad
Arbiter: description keyword, then vendor override, then NAICS-4 fallback, then residual.
Scenarios: broad component manufacturing is the seven named buckets; the residual is excluded until evidence assigns a named bucket.
Sources: (1) SAM.gov Acquisition Subaward Reporting Public API; (2) SAM.gov Entity Management API; (3) FAR 52.204-10