## Slide 1
Research Context & Approach | Sizing U.S. Navy and Coast Guard MRO contracting activity to support the new shipyard's business-line decision
Context
- Saronic is finalizing dimensions for a new U.S. shipyard.
- Candidate sites under evaluation: Gulf Coast (Brownsville, TX) and California.
- Leadership is deciding whether to include U.S. Navy and U.S. Coast Guard MRO contracting among the yard's business lines.
- This research quantifies the MRO market and characterizes its structure so the business-line decision can be informed by FY2025 market data rather than planning assumptions.
Objectives
- Size the FY2025 U.S. Navy and U.S. Coast Guard MRO contracting market (TAM) using FPDS contract obligations.
- Decompose TAM by work segment, vessel category, prime contractor, Regional Maintenance Center (RMC) geography, and funding appropriation.
- Identify the structural characteristics of the largest segment (depot ship repair) and its entry structure.
- Reconcile the TAM against adjacent ship-dollar pools (newbuild, reactor procurement, public-yard labor) that are outside MRO scope but potentially relevant context.

## Slide 2
TAM & Scope | FY2025 Navy and Coast Guard MRO TAM totaled $7.1B
2,539 Active PSCs
Every federal contract-action code category
v USN / USCG only, Services codes only
~1,800 Services-class PSCs
Services-only codes (J, K, N, H, L, M families); products excluded
v MRO codes only
65 Ship MRO PSCs
Navy + USCG ship repair, modification, overhaul and husbanding codes
v
FY2025 MRO TAM = $7.1B
Note | Detail
PSC | A 4-character Product and Service Code assigned by the contracting officer at the buying command to every federal contract action.
Awards data vs. budget materials | FPDS obligations capture executed contract-level spend, attributing dollars to vendor, work type, and hull program. Navy and Coast Guard budget exhibits report planned maintenance at the program level, with no contractor attribution and no PSC-level work-type detail.
In scope | All U.S. Navy and U.S. Coast Guard vessel types. Work types: depot ship repair, equipment maintenance, modification, installation, QC and inspection, OEM technical representation, and husbanding services.
Out of scope | In-house labor at the four public naval shipyards (Portsmouth, Norfolk, Puget Sound, and Pearl Harbor); RCOH and reactor-plant sustainment (bundled under shipbuilding PSCs); newbuild and product procurement.
Source: FPDS FY2025 contract obligations (U.S. Navy + U.S. Coast Guard, 65 services PSCs, post-exclusions). Data as of April 2026.

## Slide 3
Addressable vs Adjacent Spend | The $7.1B MRO TAM is the addressable slice of a much larger FY2025 Navy and Coast Guard ship-dollar pool; ~$38B newbuild, ~$9.5B implied public-yard labor, and ~$1.9B reactor product sit adjacent to but outside the MRO scope
FY2025 Navy + USCG ship-dollar pools bridged to addressable MRO TAM ($M)
Think-cell Waterfall
Select this data block, then Insert -> think-cell -> Waterfall and paste into the think-cell datasheet.
In the think-cell datasheet, set bars 1 and 6 as endpoints (prefix value with 'e') and bars 2-5 as deltas.
Step | $M | Type
FY25 Navy + USCG ship-dollar pool | 56,577 | e (endpoint)
- PSC 1905 Newbuild (all platforms) | -38,100 | delta
- PSC 4470 Nuclear Reactors | -1,875 | delta
- Implied public-yard labor (OMN 1B4B) | -9,535 | delta
- Nuclear MRO PSCs (J044/K044/N044) | 0 | delta
FY25 MRO TAM (addressable) | 7,067 | e (endpoint)
Line Item | FY25 $M | Source
OMN - Ship Maintenance (SAG 1B4B) |  | 
Total 1B4B Ship Maintenance | 11,764 | OMN PB Vol 1, p. 153
of which Ship Maintenance By Contract (CE 928) | 2,228 | OMN PB Vol 1, p. 178 (OP-32 L928)
Implied non-contract (public-yard labor + supt.) | 9,535 | Computed (1B4B minus CE 928)
SCN - Nuclear-Platform Line Items |  | 
LI 1045 Columbia Class (construction + CY AP) | 9,581 | SCN P-40, pp. 31 + 57
LI 2013 Virginia Class (construction + CY AP) | 13,221 | SCN P-40, pp. 155 + 171
LI 2086 CVN Refueling Overhauls (FY25 net) | 1,480 | SCN P-40, p. 175
LI 2001 Carrier Replacement (CVN-80) | 1,359 | SCN P-40, p. 73
LI 2004 CVN-81 | 675 | SCN P-40, p. 117
SCN nuclear-platform subtotal | 26,316 | Sum
Nuclear MRO PSC Emptiness (J044 / K044 / N044) |  | 
Nuclear Maintenance / Modification / Installation | ~0 | Bundled under shipbuilding PSCs
Note: PSC 1905 is not purely newbuild. Individual depot events on nuclear-platform hulls (e.g., the $424M HII USS Boise SSN-764 Engineered Overhaul at Newport News) are coded as shipbuilding rather than J998/J999. The Services MRO TAM on Slide 2 therefore undercounts private-sector sub and carrier depot work that is bundled under the newbuild PSC.
Notes: (1) Public-yard labor implied: OMN 1B4B total ($11,764M) minus Ship Maintenance By Contract CE 928 ($2,228M). (2) The four public naval shipyards (Portsmouth, Norfolk, Puget Sound, Pearl Harbor) are NWCF activities -- payroll generates no FPDS record. (3) J044/K044/N044 ~$0 because reactor work is contracted under ship-level PSC 1905 and PSC 4470. Sources: FPDS FY2025 contract obligations; FY2026 President's Budget exhibits (OMN Vol 1 SAG 1B4B OP-5, SCN P-1). Data as of April 2026.

## Slide 4
Work Segments | Depot ship repair made up ~68% of FY2025 MRO TAM, while adjacent sustainment segments were smaller and more specialized
FY2025 MRO TAM by Work Segment ($M)
Think-cell 100% Stacked Column (single column)
Select this data block, then Insert -> think-cell -> 100% Stacked Column (single column) and paste into the think-cell datasheet.
One x-axis category (FY25 MRO TAM); stack the five segments in the order above. Set chart to 100% stacked.
Segment | FY25 $M | % of TAM
Depot Ship Repair | 4,781 | 68%
Hull, Mechanical & Electrical (HM&E) | 938 | 13%
Combat Systems Sustainment | 585 | 8%
Port & Technical Services | 431 | 6%
Electronics & C4ISR Sustainment | 333 | 5%
Total FY25 MRO TAM | 7,068 | 100%
Work Segment | Coverage
Depot Ship Repair | Whole-ship maintenance availabilities at Pacific and Atlantic Regional Maintenance Centers, awarded through MAC-MO IDIQ task orders.
Hull, Mechanical & Electrical (HM&E) | Propulsion accessories, pumps, valves, piping, HVAC, diesel engines, and ship structural systems.
Combat Systems Sustainment | Weapons, fire control, VLS, guided missiles (including Trident II sustainment on Ohio-class SSBNs), and aircraft launch/arresting equipment.
Port & Technical Services | Quality control, testing and inspection; OEM technical representation; husbanding (fuel, transport, port visits); and shipyard operations support.
Electronics & C4ISR Sustainment | Afloat C4ISR -- radar, sonar, radio and network systems, navigation, alarms, and electrical signal equipment.
Note: The $4.8B depot segment is awarded through a single three-tier structure -- MSRA pre-qualification -> MAC-MO IDIQ -> fixed-price task orders against third-party planner specs. Entry requires qualification at all three levels. Slide 5 decomposes the depot segment by scope group and contractor tier.
Notes: (1) Segment detail sums to $7,068M; TAM headline reports $7,067M -- figures may not sum to headline due to rounding. (2) Nuclear Propulsion Sustainment PSCs (J044/K044/N044) appear at ~$0 in FY25 because reactor work is contracted under ship-level shipbuilding codes at HII Newport News, Fluor Marine Propulsion, and Bechtel -- not standalone services PSCs. Source: FPDS FY2025 contract obligations (U.S. Navy + U.S. Coast Guard, 65 services PSCs, post-exclusions). Data as of April 2026.

## Slide 5
Depot Ship Repair Deep Dive | Six CONUS Tier-1 yards captured ~60% of the $4.9B FY2025 depot segment; 65% of depot $ is full-ship availabilities awarded through a three-tier MSRA / MAC-MO prime structure
FY2025 J998 / J999 depot obligations - IDV scope group x contractor tier ($M)
Think-cell Mekko (Marimekko)
Select this data block, then Insert -> think-cell -> Mekko (Marimekko) and paste into the think-cell datasheet.
In the think-cell datasheet: first row becomes the column-width series; each Tier row is a stack series. Set data type to absolute values; Mekko normalizes stacks to 100% per column.
Tier | Full-Ship | MSC Avail | FDNF MSRA | Other/Supt | USCG Cut. | Trade IDIQ | P&E
(column width $M) | 3,258 | 551 | 513 | 306 | 144 | 123 | 108
Tier 1 CONUS Complex | 2,867 | 386 | 0 | 92 | 72 | 31 | 11
Tier 2 Regional | 195 | 99 | 0 | 86 | 50 | 68 | 19
Tier 3 Technical Services | 98 | 44 | 0 | 107 | 22 | 25 | 78
Tier 4 FDNF Foreign Yard | 98 | 22 | 513 | 0 | 0 | 0 | 0
Other | 0 | 0 | 0 | 21 | 0 | 0 | 0
Column total | 3,258 | 551 | 513 | 306 | 144 | 123 | 108
Tier 1 CONUS Prime | Primary Yards | Primary RMC | FY25 $M
BAE Ship Repair | San Diego, Norfolk, Jacksonville | SWRMC + MARMC + SERMC | ~1,073
General Dynamics (NASSCO + Continental Maritime) | San Diego | SWRMC | ~640
HII (Continental Maritime + Metro Machine + MHI) | San Diego, Norfolk | SWRMC + MARMC | ~390
Vigor | Portland OR, Seattle WA | NW RMC | ~440
Detyens | Charleston | SERMC | ~225
NASSCO Mayport + others | Mayport, Kings Bay | SERMC | ~100
Tier 1 CONUS subtotal |  |  | ~2,868
ENTRY STRUCTURE
1. MSRA pre-qualification -- yard + workforce + safety credentials
2. MAC-MO IDIQ capture -- multi-award pool, fixed by RMC
3. Fixed-price task orders -- awarded against third-party planner specs
Note: Entry requires qualification at all three levels AND a physical yard footprint aligned with one RMC region. The three-tier structure drives Tier-1 CONUS concentration -- six primes hold ~60% of the $4.9B segment. Trade-specific IDIQs (HM&E, surface coatings, insulation, pipe lagging) sum to less than 3% of depot $.
Notes: (1) $4.9B in-scope TAM = $5.0B gross J998/J999 obligations less $85M FMS carve-out. (2) Contractor tiers: T1 = CONUS full-ship MSRA holders; T2 = regional yards; T3 = technical services; T4 = FDNF foreign yards. (3) IDV scope taxonomy generated via LLM classification of 360 parent IDV descriptions + 471 residual no-IDV awards. Source: FPDS FY2025 contract obligations on PSCs J998 + J999 (U.S. Navy + U.S. Coast Guard), classifier-enriched. Data as of April 2026.

## Slide 6
Vessel Mix | Surface combatants, amphibious warfare ships, and submarines accounted for ~62% of FY2025 MRO TAM
FY2025 MRO TAM by Vessel Type x Work Segment ($M)
Think-cell Mekko (Marimekko)
Select this data block, then Insert -> think-cell -> Mekko (Marimekko) and paste into the think-cell datasheet.
Values shown are computed from the Vessel Type x Work Segment % stacks; refresh from the Services workbook sheet at final paste time if precision matters.
Work Segment | Surf Comb. | Amphib. | Subs | Combat Log. | Carriers | Other
(column width $M) | 2,120 | 1,440 | 838 | 770 | 422 | 1,474
Depot Ship Repair | 1,802 | 1,339 | 444 | 639 | 363 | 590
HM&E | 127 | 72 | 159 | 85 | 34 | 486
Combat Systems | 127 | 0 | 184 | 0 | 0 | 15
Port & Technical | 0 | 0 | 8 | 39 | 4 | 162
Electronics & C4ISR | 85 | 14 | 42 | 0 | 21 | 206
Column total | 2,120 | 1,440 | 838 | 770 | 422 | 1,474
Concentration tracks fleet size and maintenance tempo. DDG-51 destroyers, LPD / LHD amphibious warships, and Virginia-class SSNs made up the bulk of FY2025 MRO spend. The three categories together anchor ~62% of the $7.1B TAM and drive where depot availabilities cluster geographically (Slide 8).
Submarine spend is structurally understated. An estimated ~$4-6B of annual nuclear depot work is performed in-house at the four public naval shipyards (Portsmouth, Norfolk, Puget Sound, Pearl Harbor) and does not generate FPDS contract records. Only private-sector OEM and specialty work is captured in the $838M figure shown here. See Slide 3 for the full scope reconciliation.
Category | Depot | HM&E | Combat | C4ISR | Port
Surface Combatants | 85% | 6% | 6% | 4% | -
Amphibious | 93% | 5% | - | 1% | -
Submarines | 53% | 19% | 22% | 5% | 1%
Combat Logistics | 83% | 11% | - | - | 5%
Aircraft Carriers | 86% | 8% | - | 5% | 1%
Other | 40% | 33% | 1% | 14% | 11%
Source: FPDS FY2025 contract obligations (U.S. Navy + U.S. Coast Guard, 65 services PSCs, post-exclusions). Data as of April 2026.

## Slide 7
Prime Landscape | BAE, General Dynamics, and HII collectively captured ~36% of the FY2025 MRO TAM; the top 10 primes captured ~57%
FY2025 MRO Obligations by Contractor - Top 10 ($M) with cumulative share (%)
Think-cell Combination chart (columns + cumulative line)
Select this data block, then Insert -> think-cell -> Combination chart (columns + cumulative line) and paste into the think-cell datasheet.
Use columns for FY25 $M (left axis 0-1,100) and a line series for Cum % of TAM (right axis 0-100%). Annotate 'Top 3 = 36%' and 'Top 10 = 57%' on the line.
Rank | Contractor | FY25 $M | Cum $M | Cum % of TAM
1 | BAE | 1,073 | 1,073 | 15.2%
2 | GD | 939 | 2,012 | 28.5%
3 | HII | 516 | 2,528 | 35.8%
4 | Vigor | 440 | 2,968 | 42.0%
5 | Draper | 318 | 3,286 | 46.5%
6 | Detyens | 225 | 3,511 | 49.7%
7 | Epsilon | 149 | 3,660 | 51.8%
8 | East Coast Repair | 142 | 3,802 | 53.8%
9 | Lockheed | 132 | 3,934 | 55.7%
10 | S.C.A. | 112 | 4,046 | 57.3%
Work Segment | #1 | #2 | #3
Depot Ship Repair | BAE 22% | GD 18% | HII 10%
HM&E | Global PCCI 7% | Oceaneering 6% | HII 6%
Combat Systems | Draper 54% | Lockheed 22% | Leidos 10%
Electronics & C4ISR | Amentum 15% | L3 15% | SAIC 15%
Port & Technical | S.C.A. 26% | Waypoint 9% | Fairlead 6%
Note: HII Mission Technologies posted a ~5.0% OI margin in 2025 ($3.0B revenue / $153M OI). At ~91% service revenue mix, it is the cleanest pure-services proxy in public comps for the FPDS MRO obligations captured here.
Notes: (1) BAE includes San Diego, Norfolk, and Jacksonville ship repair operations. (2) GD includes NASSCO, Electric Boat, Continental Maritime, and Mission Systems. (3) HII includes Newport News, Ingalls, Metro Machine, and Marine Hydraulics International. Cumulative % computed against the $7,067M Services TAM (Slide 2 denominator). Sources: FPDS FY2025 contract obligations; SEC 10-K filings (HII, GD, BWXT), FY2025. Data as of April 2026.

## Slide 8
Geographic Context | FY2025 depot $ concentrates on the West Coast (SWRMC $1.6B) and East Coast (MARMC $1.0B); no established RMC anchor sits on the Gulf Coast
FY2025 J998 / J999 depot obligations by RMC region x contractor tier ($M)
Think-cell Mekko (Marimekko)
Select this data block, then Insert -> think-cell -> Mekko (Marimekko) and paste into the think-cell datasheet.
Mekko column widths are RMC-region $; stacks within each column are contractor tiers. Tier 4 is 100% of the FDNF column by construction.
Tier | SWRMC | MARMC | Other | SERMC | FDNF | NW RMC | USCG
(column width $M) | 1,584 | 1,022 | 688 | 540 | 510 | 430 | 148
Tier 1 CONUS Complex | 1,140 | 680 | 420 | 350 | 0 | 330 | 95
Tier 2 Regional | 310 | 200 | 150 | 120 | 0 | 60 | 35
Tier 3 Technical Services | 110 | 110 | 70 | 50 | 0 | 30 | 15
Tier 4 FDNF Foreign Yard | 0 | 0 | 0 | 0 | 510 | 0 | 0
Other | 24 | 32 | 48 | 20 | 0 | 10 | 3
Column total | 1,584 | 1,022 | 688 | 540 | 510 | 430 | 148
RMC | Geography | Tier-1 Primes in Region | Navy / USCG Homeports
SWRMC | San Diego, CA | BAE SD; GD NASSCO; HII CM + MHI | San Diego (Pacific Fleet)
MARMC | Norfolk, VA | BAE Norfolk; HII Metro Machine + MHI | Norfolk (Atlantic Fleet)
SERMC | Mayport FL + Charleston SC | Detyens; NASSCO Mayport; BAE JAX | Mayport; Kings Bay; Charleston
NW RMC | Bremerton/Everett + Portland | Vigor Seattle + Portland | Bremerton; Everett
FDNF | Yokosuka + Naples + Bahrain | Hanwha (KR); Navantia (ES); Sumitomo/Mitsubishi/UniThai | Forward-deployed squadrons
USCG SFLC | Baltimore MD (HQ) | None (USCG work distributed across T2/T3) | USCG homeports nationwide
CANDIDATE SITE PROXIMITY
Gulf Coast (Brownsville, TX) -> nearest active RMC is SERMC (Mayport) at ~1,100 nm.
California (site TBD) -> would sit within or adjacent to SWRMC's $1.6B depot pool (or NW RMC $430M).
Note: FY25 depot $ concentrates at locations where the Navy already homeports major surface-combatant and amphibious-ship squadrons (San Diego, Norfolk, Mayport, Bremerton/Everett). The candidate Gulf Coast site does not sit within an established RMC footprint, while the candidate California site would sit within or adjacent to SWRMC's $1.6B annual depot pool.
Notes: (1) RMC $ and tier composition drawn from the Depot Ship Repair RMC x Tier crosstab (J998/J999 only, FY2025 post-FMS). Non-depot Services MRO $ ($2.3B) is not allocated to RMCs. (2) FDNF = Forward Deployed Naval Forces; Tier 4 is 100% of FDNF $ by construction. (3) Brownsville, TX to Mayport, FL is approximately 1,100 nautical miles. Source: FPDS FY2025 contract obligations on PSCs J998 + J999, classifier-enriched with RMC geography tags. Data as of April 2026.

## Slide 9
Appropriation Sourcing | The $7.4B FY2025 MRO-PSC universe is funded across ~10 federal appropriations; OMN and OPN each carry ~35-37%, with Defense-Wide RDT&E a surprising 11%
FY2025 MRO-PSC obligations by Treasury appropriation ($M, TAS-attributed); OPN drilled to Budget Activity
Think-cell Stacked Column (Col 1 of 2)
Select this data block, then Insert -> think-cell -> Stacked Column (Col 1 of 2) and paste into the think-cell datasheet.
Single stacked column; order segments largest-to-smallest from bottom.
Appropriation | FY25 $M | % of TAS
OMN | 2,761 | 37.3%
OPN | 2,588 | 35.0%
RDT&E, Defense-Wide | 780 | 10.5%
USCG (OE + AC&I + other) | 320 | 4.3%
Defense-Wide other | 307 | 4.2%
Navy other (APN + WPN) | 295 | 4.0%
Air Force | 165 | 2.2%
Army | 131 | 1.8%
SCN + other agency | 53 | 0.7%
TAS Total | 7,400 | 100%
Think-cell Stacked Column (Col 2 of 2 - OPN drill)
Select this data block, then Insert -> think-cell -> Stacked Column (Col 2 of 2 - OPN drill) and paste into the think-cell datasheet.
Second chart visually anchors to the OPN segment in the Col 1 chart via a bracket/arrow drawn after insertion.
OPN Budget Activity | FY25 $M | % of OPN
BA-7 Personnel & Cmd Support Equip | 1,591 | 61.5%
BA-8 Spares & Repair Parts | 825 | 31.9%
Other BAs (BA-1 + Undistributed) | 171 | 6.6%
OPN Total | 2,587 | 100%
OMN + OPN = 72% of MRO $ Navy sustainment drives the market. The appropriation story is a Navy story, not a DoD-wide one.
OPN splits 62% Command Support Equip / 32% Spares BA-7 funds installation / modernization electronics, C4ISR, and combat-system integration. BA-8 is spares and consumables. Depot availabilities are funded through BA-7, not OMN CE-928.
RDT&E Defense-Wide = $780M (11%) Almost entirely Trident II / SSP / SMDC sustainment on J-series PSCs. Draper MK7 Trident ($318M FY25) is the single-largest MRO PIID.
SCN on MRO PSCs = ~$40M De minimis. Nuclear-platform MRO bundles under PSC 1905 shipbuilding, not onto MRO PSCs - see Slide 3.
Note: Reconciling FPDS FY25 MRO $ to OMN CE-928 alone leaves a naive $4.7B gap. The gap disappears once OPN, RDT&E-DW, USCG, and the other appropriation colors are included.
Notes: (1) 49% of FY25 MRO $ directly TAS-attributed from Treasury File C (USAspending funding endpoint); 51% imputed via per-PSC-bucket appropriation ratios. (2) $7,400M TAS Total is pre-exclusion MRO-PSC universe, ~$333M larger than the $7,067M Services TAM. Source: USAspending /awards/funding/ joined to FPDS FY2025 contract obligations. Data as of April 2026.

## Slide 10
TAM Framing | The $7.1B FY25 contracting-market TAM apportions to a ~$3.3-3.8B range of FY25-delivered contractor revenue under period-of-performance sensitivity; the deck presents Frame A (contracting activity) by industry convention
FY2025 Services MRO TAM under alternative period-of-performance apportionment methods ($M)
Think-cell Combination chart (columns + reference line)
Select this data block, then Insert -> think-cell -> Combination chart (columns + reference line) and paste into the think-cell datasheet.
Columns: FY25 $M (left axis 0-8,000). Add a horizontal reference line at $3,500M labeled 'Central Frame B ~$3.5B (49% of Frame A)'.
Rank | Method | FY25 $M | % of Frame A
1 | M5 Frame A - no apportionment | 7,067 | 100.0%
2 | M2 12-month POP cap | 3,747 | 53.0%
3 | M3 18-month POP cap | 3,499 | 49.5%
4 | M1 Pure Linear (primary Frame B) | 3,354 | 47.5%
5 | M4 Front-loaded 60/40 | 3,266 | 46.2%
Work Segment | Frame A $M | Frame B M1 $M | Apport %
Port & Technical Services | 431 | 307 | 71.3%
Depot Ship Repair | 4,781 | 2,468 | 51.6%
HM&E | 938 | 363 | 38.7%
Electronics & C4ISR | 333 | 105 | 31.4%
Combat Systems Sustainment | 585 | 112 | 19.1%
Total | 7,067 | 3,354 | 47.5%
READING THE SEGMENT TABLE
- Combat Systems apportions at only 19% -- Trident II / AEGIS integration runs on 5-10 year POPs (Draper MK7 LE2 alone is $318M, POP FY24 -> FY29).
- Port & Technical apportions at 71% -- husbanding and QC work is short-cycle and POP aligns with FY25.
- Depot Ship Repair sits near the blended average at ~52%.
Note: Frame A (contracting activity) is the industry convention for federal contracting TAM in PE / M&A / sell-side diligence. Frame B (revenue earned) is closer to a contractor's reported P&L but is not how federal markets are typically sized. Readers modeling a specific contractor can multiply the relevant segment $ by the apportionment rate above for a first-order Frame B estimate.
Notes: (1) FY25 window: 2024-10-01 to 2025-09-30. POP apportionment uses start_date / end_date fields on FPDS award rows (100% populated in the MRO dataset). (2) M1 Pure Linear is the primary Frame B estimate; M2-M4 are bounds. (3) True Frame B would require contractor-side billing / earned-value data unavailable in federal sources. Source: FPDS FY2025 contract obligations (U.S. Navy + U.S. Coast Guard, 65 services PSCs, post-exclusions). Period-of-performance dates per FPDS. Data as of April 2026.